## Slide 1
CS447 Recitation #3: 6/3/20
Agenda for today:
Overview of Lab #3
  These slides are available online:
  https://github.com/kc13/CS447

## Slide 2
Lab #3 highlights
Handout organization:
Pages 1-2: Description of a binary multiplication method
Page 2: Description of assignment (multiplication and exponentiation results for user’s values)

## Slide 3
Lab #3: Multiplication without using a multiplication instruction
Example: 15 x 4 in 4-bit unsigned binary
  We could run a loop to add “15” to a register 4 times.
  Alternatively, we can take advantage of the long multiplication method:
1111
x 0100
---------
0000
0000
1111
0000
-----------
0111100 = 6010

## Slide 4
Lab #3: Implementing long multiplication in assembly
1111
x 0100
---------
0000
0000
1111
0000
-----------
0111100 = 6010
This can be implemented as a loop:
Check the appropriate bit of the multiplier on each iteration (0 or 1?)
Maintain a running sum
Add 0 or the multiplicand (shifted for each new iteration)

## Slide 5
Lab #3: Helpful instructions for multiplication
1111
x 0100
---------
0000
0000
1111
0000
-----------
0111100 = 6010
Check the appropriate bit of the multiplier on each iteration (0 or 1?)
“and masks” and shifting can help you determine whether the bit in a specific position is 1 or 0
Example: Assume $t0 = 4, and I want to confirm that a ‘1’ is in Bit 2 (assuming LSB position = 0)
addi $s0, $zero, 1 #mask, 0001
srl $t2, $t0, 2 #0100 0001
and $t1, $s0, $t2 #t1 = 0001

## Slide 6
Lab #3: Implementing long multiplication in assembly
1111
x 0100
---------
0000
0000
1111
0000
-----------
0111100 = 6010
Add 0 or the multiplicand (shifted for each new iteration)
sll can perform the left shift.

## Slide 7
Lab #3: Implementing long multiplication in assembly
1111
x 0100
---------
0000
0000
1111
0000
-----------
0111100 = 6010
Maintain a running sum
For setting the loop:
In theory, the inputs could be up to 32 bits long.
The test integers will likely be no greater than 16 bits long.
The 4 bits shown here are for illustration only.

## Slide 8
Lab #3: Using multiplication to implement exponentiation
One option: Consider looping over a multiplication loop, with the result of each iteration of multiplication carried over to the next round.
See handout notes about restriction to testing small numbers.
Note this step will probably require many labels and registers. Comments can be helpful to keep track of everything.

## Slide 9
Lab #3: User interface details
Note that you are required to verify that the integers are positive.
For printing the arithmetic operators, you may find helpful syscall 11 (print character). For supplying the value to $a0, note that addi will accept character inputs (e.g., ‘=‘).
You can also use syscall 11 to print the line feed character (‘\n’).

## Slide 10
Lab #3
Remember to submit on Canvas by the deadline
Questions?