## Slide 1
CS447 Recitation #6: 6/24/20
Agenda for today:
Overview of Lab #6
  These slides are available online:
  https://github.com/kc13/CS447

## Slide 2
Lab #6 overview
Instructions PDF organization:
Pages 1-2: Introduction to Logisim
Pages 2-3: step 1: Create a 1-bit adder logic circuit
Pages 3-5: step 2: Create a 4-bit adder
Pages 5-6: Step 3: Create a combined addition and subtraction circuit, using the built-in addition and subtraction components.

## Slide 3
Logisim: Creating a basic circuit
Download: See jar file in Canvas.

## Slide 4
Logisim: Creating a basic circuit
Demo in recitation

## Slide 5
Task #1: Create a 1-bit adder circuit
This blueprint specifies exactly what needs to be done.
It can stand for one column in a multibit adder, and so it contains inputs and outputs for both A, B, and the carry-in bit.
Table from lecture slides:

## Slide 6
Task #2: Create a 4-bit adder circuit
This involves chaining together four of the 1-bit adders that you created in the first step (the blank boxes in the image).
You will need to adjust the bit width of the inputs/outputs to accommodate 4 bits.
The bold black lines indicate “splitters”, which can be used to separately route the four bits heading out of an input node (or into an output node).
The grey box at top is a constant input of 0 (see “Constant” under “Wiring”); this represents the constant 0 carry-in bit for the LSB column.

## Slide 7
Task #3: Create a combined addition/subtraction circuit
This should handle 8-bit numbers.
You will be allowed to use Logisim’s built-in adder and subtracter for this step.
The probes let you visualize the results on the wires themselves.
The multiplexer (and the operation input) serves as selector between the two inputs that could be displayed in the output node.

## Slide 8
Other Logisim tips:
If your circuit is behaving bizarrely without explanation, it may be worth trying to restart the program.
  This has been known to resolve issues in the past.
Go to Help  Library reference to learn more about the individual circuit components, and how each input/output pin is used.

## Slide 9
Questions?