## Slide 1
CS447 Recitation #8: 7/8/20
Agenda for today:
Overview of Lab #8
  These slides are available online:
  https://github.com/kc13/CS447

## Slide 2
Lab #8 overview: Building an ALU
Assignment Breakdown:
Part 1: Build a one-bit ALU
Page 2: Build a multibit ALU
Page 3: Interface with the multibit ALU from an outer “main” circuit

## Slide 3
Lab #8, Part 1: Build a one-bit ALU
Can perform:
AND,
OR,
NOR,
addition,
subtraction, set if less than (slt)
seven inputs
a, ~a, b, ~b, carryIn, operation
Less:
- for setting the
LSB for slt output
- when 1-bit ALUs are chained to produce a multibit ALU,
the other “Less” inputs will be
hard-wired to 0
three outputs
Result
Carryout
Not shown: Set
  For setting the LSB for slt output
  When 1-bit ALUs are chained together to produce a multibit ALU, the “set” output is only meaningful for the MSB (and will be used to set “Less” for the LSB)

## Slide 4
Lab #8, Part 2: Build a multi-bit ALU
Chain together 8 of the 1-bit ALUs (which will be prepared as a different subcircuit)
Note “set” output from MSB is fed into Less input for LSB; other Less inputs are set to constant values of 0.

## Slide 5
Lab #8, Part 2: Build a multi-bit ALU
Multibit subcircuit inputs:
  Four bit ALUOperation code, to be broken down (i.e., via splitter) into:
    Ainvert (for setting Ainvert in the individual bits)
    Bnegate (for setting Binvert and CarryIn for the individual bits)
    Operation (goes to the operation MUX in each bit)
Multibit subcircuit outputs:
  8-bit result
  1-bit “zero” output (indicates if the result is 0)
  1-bit overflow output
    Will require some logic to figure out if there is overflow or not (see slides from ALU slide deck)
    “set” output from MSB may need to be adjusted if overflow is present (see lecture slides)

## Slide 6
Lab #8, Part 3: Interact with the multibit subcircuit from the main canvas

## Slide 7
Questions?